China Multi Jet Vane Wheel Dry Dail Water Meter, Manufacturer, Supplier, Factory, Exporter in china

|  | Multi Jet Vane Wheel Dry Dail Water Meter APPLICATION: * Measuring the total volume of cold portable water with remote reading device passing through the pipeline, for replace Iron body, Stainless steel body water meter. FEATURES: * Body, cap, connectors' merterial are made of NYLON 66; * Multi-jet, dry-dial, easy for maintenance; * Magnetic drive reliable characteristic, long working life; * Vacuum sealed register ensures the dial keep free from fog and frost, Keep the reading clear in a long term service; * Technical data conform to international standard ISO4064 Class B; * Data Output Options:10 L/Pulse, 100 L/Pulse, or 1000 L/Pulse. * Completely plastic shell, solid and robust design, long service guaranteed; * High quality materials fiberglass reinforced polymerization amine. Maximum permissible error: * In the lower zone from qmin inclusive up to but excluding qt is 5%. * In the upper zone from qt inclusive up to and including qs is 2%; * Hot water meter 3%. MAIN TECHNICAL SPECIFICATIONS Type Size (mm) Class qs Overload Flow qp Permanent Flow qt Transitional Flow qmin Minimum Flow Minimum Reading Maximum Reading m3/h L/h m3 LXSGY-15S 15 B 3 1.5 120 30 0.0001 99,999 LXSGY-15S2 15 B 3 1.5 120 30 0.0001 99,999 LXSGY-20S 20 B 5 2.5 200 50 0.0001 99,999 LXSGY-25S 25 B 7 3.5 280.0 70 0.0001 99,999 DIMENSION Type Size Length Width Height Connecting Thread L B H d (in) mm LXSGY-15S 15 165 100 108 G3/4B LXSGY-15S2 15 190 100 108 G3/4B LXSGY-20S 20 190 99 108 G1B LXSGY-25S 25 260 105 108 G11/4B |
| --- | --- |
|  | Multi-Jet Dry Remote Reading Plastic Water Meter Product name:Multi-Jet Dry Remote Reading Plastic Water Meter Specification:LXSGY-15E~50E Type:REMOTE READING Application: *Measuring the volume of cold potable water passing through the pipeline with remote reading device FEATURES: * Dry type, magnetic drive, easy and long term clear reading, frost resistance, long working life etc. WORKING CONDITION: * Water temperature:40oC Water pressure:1.0MPa COMPLIANCE WITH STANDARD: *ISO 4064 (GB/T778-1996) MAXIMUM PERMISSIBLE ERROR: * In the lower zone from qmin inclusive up to but excluding qt is 5% * In the upper zone from qt inclusive up to and including qs is 2% Data Output Options: * 10 L/Pulse, 100 L/Pulse, or 1000 L/Pulse Working Condition : *Water temperature:40oC for cold potable water meter 90oC for cold potable water meter * Pressure:1Mpa Maximum Permissible Error: * In the lower zone from Qmin inclusive up to but excluding Qt is:Cold potable and Hot water meter5% * In the upper zone from Qt inclusive up to and including Qs is:Cold potable water meter2% Hot water meter2% |

Plastic Water Meter,plastic water meters , plastic water meter manufacturers , plastic water meter suppliers , Multi Jet Plastic Water Meter,Single Jet Plastic Dry Type Water Meter,Volumetric Plastic Water Meter,Multi Jet Water Meter,multi jet water meters , multi jet water meter manufacturer , Vane Wheel Liquid Sealed Water Meters,Multi Jet Rotary Vane Wheel Dry Water Meter,Multi Jet Rotary Vane Wheel Wet Water Meter,Vertical Type Vane Wheel Water Meters,Single Jet Water Meter,single jet water meters , single jet dry water flow meter , Single Jet Dry Type Water Meter,Single-Jet Dry Type Plastic Water Meter,Dry Type Remote Reading Plastic Water Meter,Remote Reading Water Meter,remote reading water meters , Multi Jet Vane Wheel Dry Dail Water Meter,Dry Type Remote Reading Plastic Water Meter,Volumetric Plastic Remote Reading Water Meter,Volumetric Dry Remote Reading Plastic Water Meter,Volumetric Remote Reading Water Meter,Volumetric Dry Type Remote Reading Water Meter,Rotary Postion Water Meter,rotary postion water meters , Rotary Postion Volumertic Water Meters,Volumetric Dry Type Water Meter,Volumetric Plastic Rotary Postion Water Meter,Volumetric Dry Remote Reading Plastic Water Meters,Volumetric Remote Reading Water Meters,Woltmann Water Meter,woltman water meters , woltman water meter manufacturers , woltman water meter suppliers , Horizontal Woltman Detachable Water Meter,Horizontal Woltman Type Water Meter,Vertical Woltman Detachable Water Meter,

NINGBO YUXING WATER METER CO.,LTD Add: Shangtian Town Developing Zone, Fenghua,Zhejiang, China Contact: mo Tel: +86-574-88637938 Fax: +86-574-88632638 E-mail:sales@watermeteryx.com WebSite: http://www.watermeteryx.com